## Slide 1
This Manual is for SOVOL SV01 BL Touch .
File download:https://sovol3d.com/pages/download
Scan QR code to view detailed instruction
AUTO BED LEVELING SENSOR FOR 3D PRINTER
User Manual
for SOVOL SV01 BL Touch
Facebook QR code
SHENZHEN Lian Dian Chuang Technology LTD.
Official Website: www.sovol3d.com
Tel: +86-0755-2107 4700
E-mail: sale@sovol3d.com info@sovol3d.com
www.sovol3d.com

## Slide 2
Packing List
BL Touch
Connectors
Mount
M3X6 Screws 4PCS
M3X6 Spring Washers 2PCS
BL Touch probe

## Slide 3
2.Install BLTocuh on the mount with two M3X6 screws and M3X6 Spring Washers .
1. Insert connectors into 5 Pin port.
3. Use two M3X6 screws to secure the BL Touch to the extruder mount.
② Install BLTouch
4. The cable connects to the BL Touch through the extruded back panel, secure the cable to the guide tube and cable with a cable tie and bypass the rear side of the gantry.

## Slide 4
③ Circuit Wiring
USB Cable
1. Open the base and find out the mainboard.
2. Unplug the Z limit switch (Z Port),and insert the connectors.
3. Insert connectors into the mainboard D11 pins as the picture shows.
4. Close the base.
5. Connect the computer with USB cable to update firmware .
A11
A12
D11
D12

## Slide 5
④ Update Firmware
2. Click Settings Printer Manage Printers
1.Open Cura
4. After waiting 1-3 minutes to connect the printer successfully, click “Upload custom Firmware”.
3. Click “Update Firmware”
5.Select .hex file and click “Open” to update, waiting until it is finished, then click “close”.

## Slide 6
⑤ Bed Leveling
1.Bed Leveling Level Corners, turn the bed leveling nut until the distance between the nozzle and the hot bed is about 0.2mm( the thickness of a sheet of A4 paper) (For example, figure 3), make sure that the hot bed corners are relatively flat Auto Home,and wait until it stops.
0.2mm
A4 PaPer
figure 3
2. Bed Leveling Z Offset,rotate the knob to adjust Z Offset value until the distance between the nozzle and the hot bed is about 0.2mm ( the thickness of a sheet of A4 paper) (For example, figure 3) Store settings
If the bed is relatively level, you can skip step 1.

## Slide 7
⑥ Software Settings
6、 Add G29 after G28 and click close
2.Settings→ Printer→ Manage Printers
3.Machine Settings
1.Open Cura